Centralaxonometric mapping in computer-graphics

Abstract

The degenerated projective or central-axonometric mapping of the space to the plane can be given by the images of the origin, the unit-points and the infinite points of the axes of the  Cartesian coordinate system . We will denote these points by the  symbol .

In 1910 E. Kruppa  proved that the projective mapping of a figure is projective to the central-projection of the figure. [KRU10] This affirmation can be refined, that is, it can be proved that  the projective mapping of a figure is affine to the central-projection of this figure, if the direction points  are not collinear. It is a well known fact that this predicate is not any more refinable, that is, the projective mapping of a figure is not equivalent to the central-projection of the figure. First Kruppa [KRU23] gave a synthetic condition for when a central-axonometric mapping is a central projection . For the same afffirmation J. Szabó gave several criteria which are easy to put into practice.[SZA92],[SZA93],[SZA95].

In [SZA90] J. Szabó gave an analitic method to calculate the user-coordinates of a point P(x,y,z) of the space, if the system  is given.

In this paper I will give an analytic method too, which is different from [SZA90], and maybe more applicable in computer graphics. Using homogeneous coordinates, I calculate a matrix from the given  configuration, which maps a point of the world-system to the plane.

REFERENCES

[KRU10] Kruppa E, : Zur achsonometrischen Methode der darstellenden Geometrie,Stzgsb. Ak. Wien (math.-nat.) Abt IIa, 119  (1910), 487-506

[KRU23] Müller E. - Kruppa E., Vorlesungen über darstellende Geometrie, I Bd.:
  Kruppa E.: Die linearen Abbildungen, Wien, 1923. S 183.

[SZA90] Szabó  J. : Parallele und zentrale Axonometrie, Konstruktive Geometrie Vortragssamlung Debrecen, (1990), 149-158

[SZA92] Szabó J. : Egy analitikus feltétel arra, hogy a centrálaxonometria mikor centrálprojekció, Acta Academiae Paedagogicae Nyíregyháziensis, Tomus 13/D, (1992) 89-98

[SZA94] Szabó J. : Eine analytische Bedingung dafür, da eine Zentralaxonometrie Zentralprojektion ist, Publ. Math. Debrecen, 44/3-4 (1994), 381-390

[SZA95] Szabó J.-Stachel H.-Vogel H. : Ein Satz über die Zentralaxonometrie, Stzgsb. Ak. Wien (math.-nat.) Abt IIa, 119  (1995), megjelenés alatt

[HER92] Herman I. : The Use of Projective Geometry in Computer Graphics, ISBN 3-540-55075-5 Berlin, (1992)

[ME95] Molnár E.-Ledneczky Pál. : Projective geometry in engineering, Periodica Polytechnica Ser. Eng. Vol. 99, No. 1. P43-60, (1995)

SCHWARCZ T.

Univ. Debrecen

Ins. of  Math. and Inf.

H-4010 Debrecen, POB. 12.

Hungary